## Slide 1: Bias-Free Neural Predictor
Dibakar Gope and Mikko H. Lipasti
University of Wisconsin – Madison
Championship Branch Prediction 2014

## Slide 2: Executive Summary
Problem:
Neural predictors show high accuracy
64KB restrict correlations to ~256 branches
Longer history still useful (TAGE showed that)
Bigger h/w increases power & training cost!
Goal: +
Large History
Limited H/W
Our Solution:
Filter useless context out
Notes: Here in this work, we propose BFN predictor that attempts to learn distant branch correlations by capturing only useful information in a branch predictor’s history.

## Slide 3: Key Terms
Biased– Resolve as T/NT virtually every time
Non-Biased– Resolve in both directions
Let’s see an example …

## Slide 4: Motivating Example
A
B
C
D
E
Non-Biased
Non-Biased
Biased
Biased
Biased
Left-Path
Right-Path
B, C & D provide
No
additional information
Notes: the change in the direction of the Branch A provides
sufficient evidence to cause a change in the direction of the
Branch E. In other words, the control flow through either the
Branch B or the Branches C and D in the two program paths
merely reinforces the prediction decision of the Branch E that
can independently be established by correlating only with the
non-biased branch A.

## Slide 5: Takeaway
NOT all branches provide useful context
Biased branches resolve as T/NT every time
  Contribute NO useful information
  Existing predictors include them!
Branches w/ No useful context can be omitted

## Slide 6: Biased Branches
Chart: % of Total Branches
| SPEC00 | SPEC01 | SPEC02 | SPEC03 | SPEC04 | SPEC05 | SPEC06 | SPEC07 | SPEC08 | SPEC09 | SPEC10 | SPEC11 | SPEC12 | SPEC13 | SPEC14 | SPEC15 | SPEC16 | SPEC17 | SPEC18 | SPEC19 | FP1 | FP2 | FP3 | FP4 | FP5 | INT1 | INT2 | INT3 | INT4 | INT5 | MM1 | MM2 | MM3 | MM4 | MM5 | SERV1 | SERV2 | SERV3 | SERV4 | SERV5
completely-biased(static tracking) | 36.67 | 6.69 | 34.18 | 6.4 | 5.12 | 25.8 | 70.94 | 22.47 | 50.92 | 35.43 | 49.32 | 2.88 | 1.91 | 12.14 | 19.57 | 38.39 | 51.58 | 18.97 | 0.66 | 10.8 | 65.9 | 4.25 | 2.24 | 12.15 | 19.81 | 29.96 | 20.99 | 21.2 | 42.67 | 3.52 | 18.68 | 12.44 | 63.68 | 4.6 | 26.9 | 58.14 | 60.12 | 46.92 | 57.24 | 61.65
Notes: This figure demonstrates the sizable presence of biased branches in the given traces. In other words it confirms the substantial presence of redundant information in a branch predictor’s history.

## Slide 7: Bias-Free Neural Predictor
Conventional Weight Table
…..
…..
BFN
Weight Table
Recency-Stack-like GHR
Positional History
Folded Path History
One-Dim.
Weight Table
Filter Biased Branches
GHR:
BF-GHR:

## Slide 8: Idea 1: Filtering Biased Branches
Unfiltered GHR:
1 0 1 0 0 1 0
A X Y B Z B C
Bias-Free GHR:
A B B C
1 0 1 0
Biased: B
Non-Biased: NB
NB B B NB B NB NB

## Slide 9: Idea 1: Biased Branch Detection
All branches begin being considered as biased
Branch Status Table (BST)
  Direct-mapped
  Tracks status
Notes: Probabilistic Updates/partial tags
The BFN predictor implements a direct-mapped structure BST to maintain those FSMs and classify the branches as biased or non-biased.

## Slide 10: Idea 2: Filtering Recurring Instances (I)
Minimize footprint of a branch in the history
Assists in reaching very deep into the history
Unfiltered GHR:
1 0 1 0 0 1 0
A B B C A C B
Bias-Free GHR:
A B C
1 0 0
Non-Biased:

## Slide 11: Idea 2: Filtering Recurring Instances (II)
Recency stack tracks most recent occurrence
Replace traditional GHR-like shift register
D
Q
=?
D
Q
=?
D
Q
=?
D
Q

## Slide 12: Re-learning Correlations
C
A
B
B
C
A
X
X Detected Non-biased
Bias-Free GHR:
Unfiltered GHR:
A X B C
A X B C
Table
Index
Hash Func.
1
2
3
1
3
4

## Slide 13: Idea 3: One-Dimensional Weight Table
Branches Do NOT depend on relative depths in BF-GHR
Use absolute depths to index
C
A
B
B
C
A
X
X Detected Non-biased
Bias-Free GHR:
Unfiltered GHR:
A X B C
A X B C
Table
Index
Hash Func.

## Slide 14: Idea 4: Positional History
if (Some Condition) / / Branch A
array [ 10 ] = 1;
for ( i = 0 ; i < 100 ; i ++) / / Branch L
{
if ( array [ i ] == 1 ) { ..... } / / Branch X
}
Recency-stack-like GHR capture same history across all instances
  Aliasing
Positional history solves that!
Only
One instance of X correlates w/ A

## Slide 15: Idea 5: Folded Path History
A influences B differently
  If path changes from
  M-N to X-Y
Folded history solves that
  Reduce aliasing on recent histories
  Prevent collecting noise from distant histories
N
A
M
Y
A
X
Path A-M-N
Path A-X-Y
B

## Slide 16: Conventional Perceptron Component
Some branches have
  Strong bias towards one direction
  No correlations at remote histories
Problem: BF-GHR can not outweigh bias weight during training
Solution: No filtering for few recent history bits

## Slide 17: BFN Configuration (32KB)
C
A
B
GHR:
Table
Index
Hash Func.
2-dim weight table
1-dim weight table
Z
X
Y
Loop Pred.
+
Is Loop?
Prediction
Bias-Free
Unfiltered
Unfiltered: recent 11 bits
Bias-Free: 36 bits

## Slide 18: Contributions of Optimizations
3 Optimizations : 1-dim weight table + phist + fhist
BFN (3 Optimizations) MPKI: 3.01
BFN (ghist bias-free + 3 Optimizations) MPKI: 2.88
BFN (ghist bias-free + RS+ 3 Optimizations) MPKI: 2.73
Chart: Mispredictions per 1000 Insts.
| SPEC Avg. | FP Avg. | INT Avg. | MM Avg. | SERV Avg. | Avg.
BFN (3 Optis.) | 3.5529 | 0.639 | 2.9704 | 4.2594 | 2.0426 | 3.0154
BFN(ghist bias-free + 3 Optis.) | 3.4032 | 0.4674 | 2.8344 | 4.1154 | 2.0628 | 2.8866
BFN (ghist bias-free + RS + 3 Optis.) | 3.1465 | 0.3748 | 2.7658 | 4.0942 | 2.016 | 2.7296

## Slide 19: Conclusion
Correlate only w/ non-biased branches
Recency-Stack-like policy for GHR
3 Optimizations
  one-dim weight table
  positional history
  folded path history
47 bits to reach very deep into the history