## Slide 1: Global-Local Combined Branch History The Alternative Way to Improve TAGE Branch Predictor
Yasuo Ishii

## Slide 2: Executive Summary
We submitted the perceptron inspired branch predictor in previous championships
  Fused Two Level (FTL) Branch Predictor
My early evaluation result
  2.478 MPKI (64KB FTL++ @ CBP3)
  2.365 MPKI (64KB ISL-TAGE @ CBP3)
    I give up the adder tree approach for this workshop
We provided optimized TAGE predictor
  Key Idea: Usage of the local history
  2.401 MPKI with 32KB storage budget

## Slide 3: Introduction
Branch history can be categorized into two types
  Global branch history
  Local branch history
Global history is widely used because of …
  Low cost, easy to implement, high coverage
On the other hand, local history is …
  Relatively high cost, useful in specific situation (loop)
Many predictors use local history to improve the prediction result generated from global history

## Slide 4: How to Use Local Branch History?
Two approaches
  Filter predictor : loop predictor
  Adder tree : Perceptron, PMPM, FTL, LSC-TAGE
These approaches cannot be directly applied for cascaded branch predictor (TAGE branch predictor)
Global
Predictors
Local
Predictors
+
Final prediction result

## Slide 5: Cascaded predictor: TAGE branch predictor
Multiple components use different history length
Puts high priority for components use long history
Putting appropriate priority for local history is difficult.
Base
T1
G=2
T2
G=4
T3
G=8

## Slide 6: Key Idea: Branch History Combining
Use both global history and local history for the table lookup of the tagged components
Priority of each component is not changed if the history length of Ti is longer than that of Tj (j < i)
Base
T1
G=2
T2
G=4
T3
G=8
L=0
L=0
L=1
L=2

## Slide 7: Proposal: Combined Branch History
Concatenate global history and local history with fixed ratio.
A0
A1
B0
C0
C1
D0
D1
A0
A1
B0
C0
C1
C2
D1
D0
Global history
Local history
C0
C1
A0
A1
B0
C0
C1
C2
D1
D0
+
Global-local combined history (for branch C)
Bx

## Slide 8: How to decide history length ?
Local history should be 1 / Nlht of global history
  Nlht = # of entry of local history table
A0
A1
B0
C0
C1
C2
D0
D1
A0
A1
B0
C0
C1
C2
D1
D0
Global history
Local history
4 entry
2 (= 8 / 4) bit
8 bit history
Bx
Old branch history
Disappeared
from LHT

## Slide 9: Case 1: Worked as global history
When the global history include all local history information, the combined history worked as the global history.
A0
A1
B0
C0
C1
D0
D1
A0
A1
B0
C0
C1
C2
D1
D0
Global history
Local history
C0
C1
A0
A1
B0
C0
C1
C2
D1
D0
+
Global-local combined history for C
Bx
When all local history appeared in global history, the combined history worked as the global history

## Slide 10: Case 2: Worked as local history
When the global history does not include all local history information, it helps to capture some specific control flow
A0
A1
B0
C0
C1
D0
D1
A0
A1
B0
C0
C1
C2
D1
D1
Global history
Local history
B0
Bx
A0
A1
B0
C0
C1
C2
D1
D0
+
Global-local combined history for B
Bx
When some local history did not appeared in global history, This information helps to capture the some special structure

## Slide 11: Other Optimization Techniques
Existing Optimizations
  Statistical corrector predictor
  Table Interleaving
  Loop predictor
  Special history treatment for CALL / RETURN
Additional Optimizations
  Pseudo tagged components
  Dedicated UA counter
  Tag hashing

## Slide 12: Pseudo tagged component
Pseudo tagged component is the tagged component which uses only PC for its table lookup
  It helps to reduce the performance impact of the starvation of the base component entries
Base
tagless
Tagged
G=0
Tagged
G=2
Tagged
G=4
First tagged component does not use branch history to complement the starvation of base predictor

## Slide 13: Dedicated UA Counters
TAGE predictor uses a profiling counter which tracks the usefulness of altpred for a newly allocated entry
  Altpred is the prediction result from the second longest matched tagged component
We think that the dedicated profiling for each tagged component is beneficial to improve the performance.
  We classified tagged component into 5 groups
  Provided dedicated profiling counter for each pair
    One is the longest match component, the other is the second longest match component

## Slide 14: Tag Hashing
Original TAGE uses XOR of two folded history register for the tag computation
  However, it can eliminate the information of some history information. Therefore, I add one more folded register to avoid such situation.
Tag width
Tag width - 1
Tag width - 2
XOR)
Hash Value

## Slide 15: Evaluation Result
Submitted predictor
  2.401 MPKI with 32KB budget
When the combined branch history is disabled,
  2.410 MPKI
When the other optimizations are disabled,
  2.428 MPKI
Other configuration
  3.629 MPKI with 4KB (This is not well optimized)

## Slide 16: Summary
Local history is useful, but there were no effective way to apply local history for TAGE predictor
  How to put the priority for tagged components is not clear
Solution: Combined Branch History
  Uses both global history and local history for the table lookup of the tagged components on TAGE predictor
The optimized branch predictor achieves 2.401 MPKI for 32KB storage and 3.629 MPKI for 4KB storage
  This approach is useful for the other TAGE-base predictors