## Slide 1: Temporal Stream Branch Predictor (TS Predictor)
Yongming Shen, Michael Ferdman
Notes: Hello, everyone. I’m Yongming Shen from the COMPAS lab of Stony Brook University. Today, I’ll talk about the temporal stream branch predictor, or the TS predictor for short.
This work is done in collaboration with my adviser, Mike Ferdman.

## Slide 2: Temporal Streaming
Branch predictors often repeat their mistakes
Temporal streaming can correct mistakes
  Record sequence of mistakes
  Replay sequence to apply corrections
Base | ... … | T | T | N | N | T | … …
TS | … … | 0 | 1 | 1 | 0 | 1 | … …
Corrected | … … | N | T | N | T | T | … …
Notes: The TS predictor tries to achieve high accuracy and at the same time keep things simple.
It’s design is based on two observations:
First, branch predictors often repeat their mistakes.
Second, temporal streaming can be used to correct mistakes.
This can be done by first recording a sequence of mistakes and then replay the sequence to apply corrections.
For example, suppose a base predictor makes a series of predictions and two of them are wrong.
We can record this in a temporal stream. With a 0 meaning misprediction and a 1 meaning correct prediction.
The next time the base predictor makes the same predictions, we can refer to the stream and apply corrections.

## Slide 3: The TS Predictor
Demonstrate TS branch predictor design
Prove TS effective for branch prediction
  512 KB gshare: 4.6 MPKI
  TS (512 KB gshare): 3.5 MPKI
  TS (16 KB gshare): 3.9 MPKI
  (MPKI: mispredictions per kilo-instructions)
  TS is more powerful than bigger base predictors
Notes: We made two contributions with this work.
First one is that we demonstrate how temporal streaming can be used in a branch predictor.
Second one is that we proved temporal streaming is effective for branch prediction.
When we use temporal streaming with 512 KB gshare, the MPKI for the championship traces improves from 4.675 to 3.487.
And even if we use temporal streaming with just 16 KB gshare, we still get far better performance than 512KB gshare.
This means TS is more powerful than bigger base predictors.

## Slide 4: Outline
Introduction
Predictor Design
Predictor Operation
Results
Conclusions and Future Plans
Notes: For the rest of the talk, first I’ll talk about the design of the TS predictor, then I’ll talk about the TS predictor’s operation.
After this will be results we got, and conclusions and future plans.

## Slide 5: Predictor Design
… … | 1 | 1 | 1 | 0 | 1 | 1 | 0 | 1 | … …
When to start replay?
Where to start replay?
CPU State  Base mispredict point
Replay
Fallback
Base mispredicts and
HT has suitable starting point
Replay goes wrong
Head Table (HT)
Notes: Note that for both where and when, we use base predictor mistakes as triggers.
For the design of the TS predictor.
We know we have the base predictor’s correctness history in a temporal stream, and we know that some point in time, we should should to replay from somewhere in the stream so that base predictor mistakes can be corrected.
But where should we start to replay and when should we start to replay?
Our solution for the where problem is to keep a map of cpu states to points where the base predictor made mistakes. We call this map the head table.
A CPU state could be for example a hash of global history and PC. And the base predictor misprediction points are used as potential replay starting points.
Our solution for the when problem is shown by this state machine. If the base predictor makes a mistake and there is a suitable replay point in the head table, the predictor will start replay from that point.
When replay goes wrong, the predictor will stop replay.
Note that for both where and when, we use base predictor mistakes as triggers.

## Slide 6: Predictor Design
Base Predictor
Head Table | 
Key0 | Head0
Key1 | Head1
Key2 | Head2
… … | … …
Circular Buffer |  |  |  |  |  |  |  |  | 
… … | 1 | 1 | 1 | 0 | 1 | 1 | 0 |  | … …

Tail
Head

Notes: Corresponding to the big picture design, the TS predictor has three components.
First there is the base predictor, which provides base predictions.
Then there is the circular buffer, which records the base predictor’s correctness. A 1 in the buffer means correct, a 0 in the buffer means incorrect.
New history will be stored at the tail pointer, and old history will be read from the head pointer.
Finally there is the head table, which maps CPU states to potential replay starting points.

## Slide 7: Predictor Operation
Base predictor
  Updated independently
Record
  Correctness of base predictor (Circular Buffer)
  Potential replay starting points (Head Table)
Replay Mode
  Will use history to correct base predictions
  More replay, more errors corrected
Fallback Mode
  Pass on base prediction
  Predictor starts in Fallback mode
Notes: Now a big picture of the TS predictor’s operation.
First, the predictor will update the base predictor independent of all the temporal streaming parts and effects.
Second, the predictor will keep recording two kind of things. One is the the base predictors correctness, which goes to the circular buffer. Second is potential replay starting points, which goes to the head table.
When the predictor makes predictions, it could be in one of two modes, replay mode or fallback mode.
If the predictor is in replay mode, it will refer to history in the circular buffer to correct the base predictor’s mistakes. Note that the more time the predictor spends in replay mode, the more errors will get corrected, and the more benefit we can get from temporal streaming.
If the predictor is in fallback mode, it will just pass on the base predictor’s predictions. When the predictor starts, it is initialized to be in fallback mode.
Now I’ll give more details on several parts of the TS predictor’s operation.

## Slide 8: Record: Circular Buffer
“1” for correct, “0” for incorrect
Base Predictor
Circular Buffer |  |  |  |  |  |  |  |  | 
… … | 1 | 1 | 1 | 0 | 1 | 1 |  |  | … …

Tail
taken
0
Notes: First, let’s take a closer look at the circular buffer.
After each prediction, the circular buffer will record the correctness of the base predictor under the tail pointer, and then advance the tail pointer.
A “1” in the buffer means correct, a “0” in the buffer means incorrect.
In this example, the base predictor says taken, which is a mistake, so a 0 is written.

## Slide 9: Record: Head Table
Updated whenever base predictor makes a mistake
Base Predictor
Head Table | 
Key0 | Head0
Key1 | Tail
Key2 | Head2
… … | … …
Circular Buffer |  |  |  |  |  |  |  |  | 
… … | 1 | 1 | 1 | 0 | 1 | 1 | 0 |  | … …

Tail
taken
Hash(CPU State)
Notes: Now let’s look at the head table.
Whenever the base predictor makes a mistake, the head table will be updated.
And here’s how it works.
First, the current CPU state will be hashed to get a key.
Then an entry mapping the key to the current tail position will be inserted into the head table.
If an entry with the same key already exists, it will be overridden.

## Slide 10: Replay Mode
Go from Fallback to Replay mode
  Base predictor makes a mistake
  Head table has entry
Base Predictor
Head Table | 
Key0 | Head0
Key1 | Head1 <= Tail
Key2 | Head2
… … | … …
Circular Buffer |  |  |  |  |  |  |  |  | 
… … | 1 | 1 | 1 | 0 | 1 | 1 | 0 |  | … …

Tail
taken
Head (Set to Head1)

Hash(CPU State)
Notes: Now let’s talk about replay mode, which is the most important part of the TS predictor’s operation.
For the predictor to go from fallback to replay, two conditions must be met.
First is the base predictor makes a mistake, second is the hash of the current CPU state has a corresponding entry in the Head table.
Here’s an example of how the predictor transitions into replay mode.
First, the base predictor makes a mistake, so a 0 is recorded in the circular buffer and the tail pointer is advanced.
Now triggered by the base predictor’s mistake, the TS predictor will try to enter replay mode.
To do so, it will first compute a hash of the current CPU state and get a key. In this case the key is Key1. Then it will look up the head table for a Key1 entry.
In this case an entry is found, and its value is Head1. So the head pointer is set to Head1, replay will start from there, and mode transition is complete.
Note that the base predictor mistake will also trigger a head table update, but head table update happens after mode transition.

## Slide 11: Replay Mode
While replaying, history is used to correct mistakes
  “0” means flip base prediction
  “1” means pass on base prediction
Head pointer advances on each prediction
  Even after base predictor makes a mistake
Buffer | ... … | 0 | 1 | 1 | 0 | 1 | … …
Base | … … | T | T | N | N | T | … …
Corrected | … … | N | T | N | T | T | … …
Head

Notes: While replaying, history is used to correct mistakes.
For each prediction, the TS predictor will first get the base prediction, and then get the history bit under the head pointer.
If the history bit is 0, the base prediction will be flipped, otherwise it is passed on.
The head pointer will be advanced after each prediction.
Note that this happens even if the base predictor makes mistakes, which means while in replay mode, base mistakes won’t trigger head table lookup and head pointer reset.

## Slide 12: Fallback Mode
Transition from Replay to Fallback mode
  Base prediction erroneously flipped
  Base prediction erroneously passed on
During Fallback mode
  Pass on base predictor output
Record into Circular Buffer and Head Table continues
Notes: Things for Fallback are simpler.
If replay goes wrong during replay mode, the TS predictor will drop to fallback mode.
Replay goes wrong means either the base prediction is flipped but turns out to be correct, or base prediction is passed on but turns out to be wrong.
In fallback mode, the TS predictor will just pass on the base predictor’s output.
Also note that the TS predictor will continue to do recording while in fallback mode.
This ends the description of the TS predictor’s operation.

## Slide 13: Outline
Introduction
Predictor Design
Predictor Operation
Results
Conclusions and Future Plans
Notes: Now we will talk about results and conclusions.

## Slide 14: Submitted Implementation
Unlimited memory track
Base predictor: 512KB gshare
Circular Buffer: unlimited size
Head Table: unlimited size
Hash function: 140-bit global history ++ PC
Notes: Our submission is for the unlimited memory track.
For this submission, we used a 512 KB gshare predictor as the base predictor.
Both the circular buffer and the head table are of unlimited size.
And the hash function concatenates 140-bit of global history with the PC to generate keys.

## Slide 15: Predictor Accuracies
  Our Score: 3.487 MPKI
Chart: gshare memory size
| 16KB | 32KB | 64KB | 128KB | 256KB | 512KB | 1MB | 2MB | 4MB
gshare | 5.53 | 5.196 | 4.971 | 4.823 | 4.768 | 4.675 | 4.643 | 4.612 | 4.586
Temporal Stream (gshare) | 3.897 | 3.695 | 3.575 | 3.517 | 3.505 | 3.487 | 3.507 | 3.537 | 3.577
Notes: And here are our results.
In this graph, red bars represent gshare’s accuracies, and blue bars represent the TS predictor’s accuracies. The lower the bar, the better the accuracy.
The x-axis represent the memory size of the gshare predictor, or in the case of the TS predictor, the memory size of its base gshare predictor.
The y-axis is accuracy measured by MPKI, mispredictions per kilo-instructions.
As can be seen from this chart, the TS predictor consistently outperforms the gshare predictor, and even 16KB TS does better than 4MB gshare.
The score for our final submission is 3.487 MPKI.

## Slide 16: Conclusions and Future Plans
Temporal streaming is useful for branch prediction
Many opportunities for improvement
  Current design is proof of concept
  Compact designs possible
  Improved head indexing
  Alternative base predictors
  yoshen@cs.stonybrook.edu
4 | 3 | 1
1 | 1 | 1 | 1 | 0 | 1 | 1 | 1 | 0 | 1
TS (256KB, including gshare) :
3.7MPKI
Notes: In conclusion, we showed that temporal streaming is useful for branch prediction.
The current design of the TS predictor is pretty simple, and there are a lot of space for improvement.
In the future, we will explore limited memory implementations of the TS predictor, different head table indexing schemes, and alternative base predictors.
For limited memory implementation, because the base predictor is correct most of the time, the temporal stream can be efficiently compressed by aggregating long sequences of 1’s in to integers.
Using this simple compression scheme, we can achieve 3.7 MPKI using 256 KB of memory.