## Slide 1: Combining Local and Global History for High Performance Data Prefetching
Martin Dimitrov and Huiyang Zhou

## Slide 2: Our Contributions
New localities in the local and global address stream
A high performance prefetcher design
Mechanisms for eliminating redundant prefetches
Advocating for L1-cache data prefetchers

## Slide 3: Presentation Outline
Contributions
Novel data localities in the address stream
Proposed data prefetcher
Filtering of redundant prefetches
Design Space Exploration
Experimental Results
Conclusions

## Slide 4: Novel Data Localities: Global Stride
Global Stride exists when there is a constant stride between addresses of two different instructions.
global address stream 
Load A: X Y Z
Load B: X+d Y+d Z+d
When does it occur
  Load/store instructions access adjacent elements of a data structure
  Address-Value Delta [MICRO-38] is also a form of global stride
Notes: Address value delta (AVD) can also detect global strides in some cases, such as elements of the same data structure. However, AVG depends on the way memory was allocated.

## Slide 5: Novel Data Localities: Most Common Stride
Most Common Stride exists when a constant pattern is disrupted from time to time.
local address delta stream 
Store A: D X D Y D Z D …
When does it occur
for (j = lll = 0; j < ll; ++j){ x = psv->value(j); if (isNotZero(x, eps)){ k = psv->index(j); kk = u.row.start[k] + (u.row.len[k]++); u.col.idx[m++] = k; u.row.idx[kk] = i; u.row.val[kk] = x; ++lll; ...
68 47316 68 47212 68 47236 68 47068 68 47164 68 47132 68 47356 68
Code example from Soplex
Local address delta in bytes
Notes: When does it occur
  When the for-loop iterates, the kk values are a constant stride apart. In this case j is usually 2 (we loop only twice)
  The next invocation of the for-loop, a different set of addresses are manipulated

## Slide 6: Novel Data Localities: Scalar Stride
Scalar Stride exists when the address is multiplied or divided by a constant
local address stream 
Load A: 32D 16D 8D 4D 2D D …
When does it occur
long cmp; while ( ... ){ ... cmp *= 2; if( cmp + 1 <= net->max_residual_new_m ) if( new[cmp-1].flow < new[cmp].flow ) cmp++; }
576 768 1600 3200 6336 12672 25344 50688 101440 202880 405696 811392 1622784 3245632 6491200 12982464 25964864 51929728 103859456 207718976 415437888
Code example from mcf
Local address delta in bytes

## Slide 7: Proposed Data Prefetcher
GHB (N entries)
Prefetch Function
Prefetch requests
PC
Last addr
Last matched stride
LDB (FIFO)
...
Index<N-1
Index-N
Few static instructions may occupy the whole GHB
Requires sequential traversal of the linked list
Filtering Redundant Prefetches
Tag
Index
PC
Index Table
Global History Buffer (GHB) Prefetcher
Notes: Describe the basic operation of GHB
Point out the weaknesses of the GHB
Introduce our LDBs: Explain how they address the deficiencies of the GHB. We allocate an LDB for each of the most commonly misses load/store. This way, those load/store will go to the LDB without polluting the GHB and without linked list traversal.
Explain that either the GHB or the LDB will provide a history of strides to the prefetch function. The prefetch function will search for patterns in those strides. We explain that later.
The final component of our design in the filtering of rdundant prefetches

## Slide 8: Prefetch Function Detecting Global Stride
global address stream 
Load A: X Y Z
Load B: X+d Y+d Z+d
GHB (N entries)
Y+d
Z+d
X
Y
Z
-
-
Match ?
Global delta
Global delta

## Slide 9: Prefetch Function Detecting Delta Correlation
local delta stream 
Load A:
a b c d a b c d a b c d . . .
a b
a b c d  generate prefetches
Match !

## Slide 10: Prefetch Function Detecting Single Delta Match
local delta stream 
Load A:
a x c d a z c d a y c d . . .
a
a x c d  generate prefetches
Match !

## Slide 11: Prefetch Function
If no delta correlation is detected, generate 2 prefetches
  Prefetch last matched stride to approximate most common stride.
  Next line prefetch
The output of the prefetch function is a buffer (up to max prefetch degree) filled with potential prefetch addresses.
Notes: * Point out that some of those prefetch addresses may be redundant and next, we explain how to deal with redundant prefetches.

## Slide 12: Filtering of Redundant Prefetches
Local redundant prefetches
Load A address stream
miss: a
prefetch: b, c, d, e
time 1:
hit (pref bit ON): b
prefetch: c, d, e, f
time 2:
hit (pref bit ON): c
prefetch: d, e, f, g
time 3:
Global redundant prefetches
Load B prefetches: a+8, x, y, etc.
Other loads/stores use data in the same cache line as Load A.
Load C prefetches: b+16, w, z, etc.

## Slide 13: Filtering of Redundant Prefetches
Filtering local redundant prefetches
  Add a confidence bit to each LDB to indicate that we have already prefetched the full prefetch degree
  If conf bit is set, make only 1 prefetch
Load A address stream
miss: a
prefetch: b, c, d, e
time 1:
hit (pref bit ON): b
prefetch: f
time 2:
Filtering global redundant prefetches
  Use a MSHR
  Use a Bloom filter. On a Bloom filter hit, drop the prefetch. Reset the Bloom filter periodically.
conf: ON
conf: ON

## Slide 14: Design Space Exploration Prefetch into the L1 or L2 Cache ?
We advocate for prefetching into the L1 cache
  L1-cache hits are better than L2-cache hits
  More accurate address stream
  Access to the program counter (PC)
  Latency is more critical

## Slide 15: Design Space Exploration Three Prefetcher Design Points
GHB-LDB-v1: Highest performance design, using MSHRs to remove redundant prefetches.
GHB-LDB-v2: Scaled down design, using Bloom filter to remove redundant prefetches.
LDB-only: Very complexity and latency efficient design.

## Slide 16: Design Space Exploration LDB-only Design
Each entry in the table is an LDB. (a FIFO of last several deltas, last address and a confidence bit)
Can detect all the stride patterns, except global stride
Latency efficient: no linked list traversal, quick Bloom filter access
Tag
LDB
PC
LDB Table
Prefetch Function
Prefetch requests
Bloom Filter

## Slide 17: Storage Cost
Storage Cost | GHB-LDB-1 | GHB-LDB-2 | LDB-only
Index Table | 256-entry 8-way 9728 bits | 256-entry 8-way 9728 bits | 64-entry 8-way
GHB | 192 entry 192 * (32+8) = 7680 bits | 128 entry 128 * (32+7) = 4992 bits | N/A
Prefetch Func. | 1120 bits | 1120 bits | 1120 bits
Prefetch MSHR | 256-entry 8-way 256*(21+3)=6144 bits | N/A | N/A
Bloom filter | N/A | 2048 + 8-bit reset counter | 4096 + 9-bit reset counter
LDBs | 16 LDBs 16*(7*32+32+32+32+5) =5200 bits | 16 LDBs 16*(7*32+32+32+32+4+1)=5200 bits | 64 LDBs 64*(7*24+32+32+3+1) =15104 bits
Counters | 100 bits | 100 bits | N/A
Total | 29972 bits (3.7kB) | 23196 bits (2.9kB) | 20329 bits (2kB)

## Slide 18: Experimental Results
Speedup for best performing design point GHB-LDB-v1
Speedup | bzip2 | lbm | mcf | milc | omnetpp | soplex | xalan | Gmean
Conf1 | 1.07 | 2.89 | 2.65 | 1.97 | 1.13 | 1.54 | 0.99 | 1.61
Conf2 | 1.08 | 2.98 | 1.90 | 2.83 | 1.10 | 1.46 | 0.97 | 1.60
Conf3 | 1.02 | 2.98 | 1.88 | 2.83 | 1.11 | 1.48 | 1.37 | 1.67
Avg. speedup for other two designs: 1.60X and 1.56X

## Slide 19: Conclusions
We introduce a high performance prefetcher design for prefetching into the L1 cache.
Discover and utilize novel localities in the global and local address streams
Emphasize the importance of filtering redundant prefetches and proposing mechanisms to accomplish the task

## Slide 20: Questions?

## Slide 21: Backup: Experimental Results
Speedup for best performing design point GHB-LDB-v1
Speedup for best performing design point GHB-LDB-v1, prefetching into the L2 cache*
Speedup | bzip2 | lbm | mcf | milc | omnetpp | soplex | xalan | Gmean
Conf1 | 1.07 | 2.89 | 2.65 | 1.97 | 1.13 | 1.54 | 0.99 | 1.61
Conf2 | 1.08 | 2.98 | 1.90 | 2.83 | 1.10 | 1.46 | 0.97 | 1.60
Conf3 | 1.02 | 2.98 | 1.88 | 2.83 | 1.11 | 1.48 | 1.37 | 1.67
Speedup | bzip2 | lbm | mcf | milc | omnetpp | soplex | xalan | Gmean
Conf1 | 1.05 | 1.93 | 1.84 | 1.86 | 1.14 | 1.37 | 0.97 | 1.40
Conf2 | 1.06 | 2.40 | 1.68 | 2.68 | 1.08 | 1.49 | 0.95 | 1.51
Conf3 | 1.02 | 2.40 | 1.67 | 2.68 | 1.10 | 1.46 | 1.32 | 1.57
*Due to a problem with our MSHR implementation while prefetching into the L2-cache, we use a Bloom filter.

## Slide 22: Backup: Experimental Results
Speedup for GHB-LDB-v1, no filtering of redundant prefetches
Speedup for original GHB design, prefetching into L1, no filtering of redundant prefetches
Speedup | bzip2 | lbm | mcf | milc | omnetpp | soplex | xalan | Gmean
Conf1 | 1.07 | 2.89 | 2.64 | 1.97 | 1.18 | 1.55 | 0.99 | 1.62
Conf2 | 1.07 | 0.51 | 0.91 | 2.72 | 1.11 | 1.15 | 0.96 | 1.07
Conf3 | 0.96 | 0.51 | 0.91 | 2.70 | 1.11 | 1.18 | 1.42 | 1.12
Speedup | bzip2 | lbm | mcf | milc | omnetpp | soplex | xalan | Gmean
Conf1 | 1.06 | 2.89 | 2.40 | 1.96 | 1.10 | 1.30 | 0.83 | 1.50
Conf2 | 1.06 | 0.66 | 0.94 | 2.15 | 1.07 | 1.11 | 0.77 | 1.04
Conf3 | 1.03 | 0.65 | 0.94 | 2.15 | 1.08 | 1.15 | 1.11 | 1.09
*Due to a problem with our MSHR implementation, when prefetching into the L2-cache, we use a Bloom filter.

## Slide 23: Backup: Experimental Results
Speedup for GHB-LDB-v2
Speedup | bzip2 | lbm | mcf | milc | omnetpp | soplex | xalan | Gmean
Conf1 | 1.07 | 2.88 | 2.53 | 1.95 | 1.17 | 1.48 | 0.97 | 1.59
Conf2 | 1.08 | 2.77 | 1.84 | 2.78 | 1.12 | 1.47 | 0.94 | 1.57
Conf3 | 1.01 | 2.80 | 1.83 | 2.78 | 1.13 | 1.51 | 1.37 | 1.65
Speedup | bzip2 | lbm | mcf | milc | omnetpp | soplex | xalan | Gmean
Conf1 | 1.07 | 2.83 | 2.38 | 1.91 | 1.13 | 1.47 | 0.89 | 1.54
Conf2 | 1.08 | 2.92 | 1.85 | 2.48 | 1.09 | 1.47 | 0.85 | 1.53
Conf3 | 1.04 | 2.91 | 1.84 | 2.48 | 1.10 | 1.55 | 1.30 | 1.63
Speedup for LDB