## Slide 1: Perceptron Branch Prediction with Separated T/NT Weight Tables
Guangyu Shi and Mikko Lipasti
University of Wisconsin-Madison
June 4, 2011

## Slide 2: Perceptron Branch Prediction
Perceptron branch predictor [Jiménez & Lin, 2001]
7 4 -8 -3 -5
PC
1 -1 1 -1 -1
History
*
>=0
3
Y
Taken
6 5 -9 -2 -4
-2
N
Not-taken
Outcome: Not-taken

## Slide 3: Intuition
A code example:
To predict branch B:
  If A is taken, B is also taken for sure
  If A is not taken, do not know the outcome of B
If A is taken at certain frequency, then whenever A is not-taken, B will be predicted “not-taken”.
… // x is an unknown value
if (x>1000) // Branch A { /* do something …*/}
if (x>500) // Branch B { /* do something else… */}

## Slide 4: Intuition
Perceptrons can represent positive or negative correlations between branch B and past branches.
They cannot strengthen 1(2) without strengthen 4(3), or vice versa
T
NT
T
NT
… // x is an unknown value
if (x>1000) // Branch A { /* do something …*/}
if (x>500) // Branch B { /* do something else… */}
1
2
3
4

## Slide 5: SWP: Separated Weight Predictor
Separate T/NT weight tables
Prediction Algorithm:
function predict: boolean
begin
sum := 0;
index := hash (PC);
for i in 1 to ghl do
if GHR[i] = true then
sum := sum + WT[index, i];
else
sum := sum + WNT[index, i];
end for
predict := (sum>=0);
end
1
0
1
1
0
WT
WNT

## Slide 6: SWP: Separated Weight Predictor
Update Algorithm
function update begin
if |sum|<threshold or predict != br_taken
index := hash (PC);
for i in 1..ghl do
if {GHR[i] , br_taken} = {1, 1} then
WT[index,i] := WT[index,i] +1;
if {GHR[i] , br_taken} = {1, 0} then
WT[index,i] := WT[index,i] -1;
if {GHR[i] , br_taken} = {0, 1} then
WNT[index,i] := WNT[index,i] +1;
if {GHR[i] , br_taken} = {0, 0} then
WNT[index,i] := WNT[index,i] -1;
end for
end if
end
1
0
1
1
0
WT
WNT

## Slide 7: SWP: Separated Weight Predictor
Capable of prediction some linearly inseparable branches even if path information is the same
1 -1(0)
History
-3 -1
Perceptron
Prediction: -3 – (-1) = -2 Not-taken

## Slide 8: SWP: Separated Weight Predictor
Capable of prediction some linearly inseparable branches even if path information is the same
1 -1(0)
1 -2
4 -1
History
SWP
Prediction: 1+(-1) = 0 (Taken)

## Slide 9: SWP: Separated Weight Predictor
Combined with other optimization schemes
  Piecewise linear branch prediction [Jiménez, 2005]
  Dynamic threshold from O-GEHL [Seznec, 2005]
Bias weights are removed

## Slide 10: Implementation of SWP
Additional multiplexors (in parallel)
No bitwise complement of weights needed

## Slide 11: Simulation Result
Performance result of 11 traces out of 40 (in MPPKI)

## Slide 12: Optimization for space
Space inefficient: 2x storage space of the regular perceptron predictor.
Solution: Partially separated weight tables
WT
WNT
W
PC
Path
XOR
1 0 0 1 … 0
0 1 1 0 … 1
1 1 -1 1 … -1
*
*
*
History 1 to h0
History h0+1 to h

## Slide 13: Optimization for space
Simulation result on branch prediction with partially separated weight tables (in MPPKI)

## Slide 14: Configuration for CBP-3
Final configuration: 3 different weight tables
  First 20 branches: separated weights, 1024 entries
  Next 16 branches: single weight, 1024 entries
  Last 29 branches: single weight, 512 entries
  Total history length: 65
  Total size of the weight tables: 61.7KB

## Slide 15: Future work
Analyze how often is code example 1 executed
Further reduce the storage budget by using adaptive encoding algorithm