## Slide 1: A Penalty-Sensitive Branch Predictor
Yue Hu
David M. Koppelman
Lu Peng
Department of Electrical and Computer Engineering
Louisiana State University .
Notes: Good afternoon. My name is Yue Hu. Today I’d like to talk about “A Penalty-Sensitive Branch Predictor”. First, let’s have a look at our motivation.

## Slide 2
Why not favor HP branches to decrease their MR?
1. Motivation
Typical branch predictor: to decrease misprediction rate (MR):
i.e. Two-level adaptive (Yeh & Patt), Neural (Vintan & Jimenez) and LTAGE (Seznec)
Performance can also be improved even if MR doesn’t decrease
Even if total MR doesn't decrease, performance could still be improved
Time
Run 1
Run 2
Time that a mispredicted branch is on the wrong path
However
High penalty (HP)
Low penalty (HP)
The same program on the same computers but different branch predictors
Notes: As we all know, in the past several decades, researchers on branch predictors have been making great efforts to decrease misprediction rate. Such as Two-level adaptive predictor, Neural predictor and LTAGE predictor. No one can deny that great performance improvement has been achieved from these design.
However, performance can also be improved even if MR doesn’t decrease. Take this diagram for example. It shows two running time of the same program on the same computers but different branch predictors. The red and green blocks mean the time that a mispredicted branch is on the wrong path. The red is for high-penalty branches. The green is for low-penalty branches. The black and white one means other running time.
As we can see, both two runs have four misprediction. However, run 2 is better. This is because compared with run1, although run2 also has four misprediction, it has less high-penalty one which is more harmful. So, why not favor high-penalty branches to decrease their MR so that even if the total MR doesn’t decrease, performance could still be improved.
Based on this motivation, we implemented our penalty-sensitive predictor. Now, let me introduce our design.

## Slide 3
1
2
3
1: Predict a branch: HP or LP?
2: Based on TAGE, can favor HP branches, while only provide normal operation for LP branches;
3: Enabled only when beneficial.
Design Overview
2. Design Overview
Main predictor
Assistant predictor
Figure 1. Overall structure of our predictor
Notes: This is the overall structure of our predictor. It’s composed of three sub-predictors. The first one is penalty predictor which can predict a branch whether it is HP or LP. The second is Two-class TAGE predictor which is based on TAGE. It can favor HP branches, while only provide normal operation to LP branches. These two sub-predictors work together as our main predictor. The third is loop predictor which works as an assistant. It is enabled only when beneficial.
Next, I’d like to introduce the main predictor in detail. The loop predictor is skipped here.

## Slide 4
…
Penalty table
8-bit penalty counter (CNT)
1-bit penalty state (STA)
Design Overview
2.1 Penalty Predictor
CNT = 0;
STA = LP
Penalty
>= 120 cyc?
CNT += 8;
CNT --;
Yes
No
CNT >= 192?
STA = HP
Yes
No
CNT == 0?
STA = LP
Yes
No
High-penalty state remains at least hundreds of executions, so the following HP branches can get benefits.
Notes: The penalty predictor is composed of a penalty table. Each entry has an 8-bit penalty counter and a 1-bit penalty state.
Initially, the CNT and STA are reset to 0 and LP individually. For each branch, at retire stage, we check its penalty, the cycles between its fetch and retire stages. If it is less than 120 cycles, then the CNT minus one. Otherwise it plus eight.
Once the CNT increases to 192, the STA will transfer to HP. It won’t return to LP until the CNT decreases to 0 again. Once a branch is predicted as HP. This HP state will remain at least hundreds of execution so the following HP branches can get benefit.

## Slide 5
2-bit bimodal
predictor
3-bit
pred
2-bit
use (U)
[9-16]-bit
tag
Hash (His, PC)  Index: direct to one entry in each bank;
wider tag
Prediction:
Higher bank: longer history, wider tag -> more accurate
Design Overview
2.2 Two-class TAGE Predictor
 Tag: check whether hit (H) or miss (M);
U0
U2
U0
U1
U1
U1
H
M
H
M
M
M
M
Final Prediction
[Only rough idea]
Notes: Let’s have a look at the other part of the main predictor—Two-class TAGE predictor. Because of its high-complexity, only rough idea is shown here.
It is composed of several banks. Bank0 is a 2-bit bimodal predictor. Bank 1-6 are TAGE predictors. Each entry has a varied-length tag, a 3-bit prediction counter, and a 2-bit useful counter.
When giving a prediction, the hash function will generate an index, direct to one entry in each bank. These highlighted entries are indexed. The number after U is the value of useful counter. “0” means useless. Positive means useful. Also a tag, to check whether these entries are hit or miss. As we can see, bank0 and bank2 are hit. Since higher-numbered banks use longer successive history, and have wider tag, therefore, it may be more accurate for certain branches. So bank2 will give the final prediction.

## Slide 6
Update:
New entries allocated at higher banks when mispred.
LP: only one entry allocated;
HP: a second entry allocated with two limitations
1. A bank with a useless entry;
Design Overview
2.2 Two-class TAGE Predictor
mispred
Since occupied, not used.
First allocation here
HP’s double-entry allocation doesn’t harm that of LP too much
Since occupied, not used.
Second allocation here for HP
2. Last two allocations in the bank are
one-entry allocations;
Notes: Let’s introduce its update in which our favoring mechanism is embedded.
New entries will be allocated at higher-numbered banks when mispredicted. Suppose bank2 mispredicted. If this mispredicted branch is a low-penalty one, then only one entry is allocated. First, we check bank3, since the indexed entry is useful, therefore, we skip it and check that of bank4. It is a useless entry, so first allocation here. This is the update mechanism for LP branches.
How about a HP branch? For a HP branch, a second entry will be allocated but with two limitations. First, there should be a bank with a useless entry. We continue to check bank5, since occupied, not used. Bank6, the entry is useless. So now we find the bank with a useless entry. The second limitation is :last two allocations in this bank are one-entry allocations. Supposed this is the case, then a second entry will be allocated in bank 6.
These limitation are carefully chosen, so that HP branches’ double-entry allocations doesn’t harm that of LP branches too much.

## Slide 7
Update:
Design Overview
2.2 Two-class TAGE Predictor
mispred
Since occupied, not used.
First allocation here
Double-entry allocation favors HP branches so that their new entries can survive longer time to establish their usefulness.
Since occupied, not used.
Second allocation here for HP
Two cases for U0
1. Entry itself is not recently useful, if ever;
2. New allocation, usefulness hasn’t been established
Notes: Just as we said, when useful counter is 0, it may be kicked out by other branches. There are two cases when useful counter is 0. The first one is the entry itself is not recently useful, if ever. The second is it is a new allocation. It’s usefulness hasn’t been established yet. For the second case, the prediction accuracy will be decreased. However, if we allocate two entries, then even if one entry get kicked out, we still have another entry. This is the way we favor HP branches.

## Slide 8
Chart: 
| CL01 | CL02 | CL03 | CL04 | CL05 | CL06 | CL07 | CL08 | CL09 | CL10 | CL11 | CL12 | CL13 | CL14 | CL15 | CL16 | INT01 | INT02 | INT03 | INT04 | INT05 | INT06 | MM01 | MM02 | MM03 | MM04 | MM05 | MM06 | MM07 | SER01 | SER02 | SER03 | SER04 | SER05 | WS01 | WS02 | WS03 | WS04 | WS05 | WS06 | Average
Correct_Pre_H | 55.5 | 85.8 | 13.6 | 70.5 | 29.3 | 0 | 20.2 | 3.3 | 8.9 | 33.5 | 16.9 | 22.5 | 23.2 | 34 | 34.5 | 38.9 | 9.2 | 6.5 | 33.8 | 0 | 13.1 | 14.5 | 19.4 | 18.4 | 28.6 | 22 | 11.7 | 19.7 | 86.1 | 14.7 | 25.1 | 25.2 | 22.2 | 33.5 | 21.6 | 30.5 | 54 | 6.5 | 34.1 | 17.7 | 26.4675
Total_Pred_H | 23.5 | 1.8 | 25 | 8.8 | 33.6 | 0 | 23 | 3.5 | 9 | 44 | 5.6 | 46.6 | 31.4 | 27.4 | 26.9 | 23 | 19.4 | 14.8 | 25 | 0 | 9.9 | 11.3 | 11.8 | 11.6 | 28.2 | 27.7 | 13.7 | 54.1 | 13.2 | 18.7 | 56.3 | 55.6 | 43.1 | 43.2 | 36.4 | 28.3 | 45.2 | 4.6 | 33.9 | 9.4 | 23.7125
FN | -0.9 | -0.6 | -2.3 | -0.3 | -2.3 | 0 | -1.7 | -0.5 | -0.7 | -1.7 | -0.9 | -2.3 | -2.5 | -1.4 | -1.4 | -1.5 | -1.6 | -1.6 | 0 | -0.1 | -1.3 | -1.4 | -1.5 | -1.6 | -2 | -1.8 | -0.5 | -0.3 | -0.1 | -2.3 | -2.1 | -2 | -2.3 | -1.8 | -1.9 | -2 | -0.1 | -0.8 | -1.9 | -1.3 | -1.3325
1. predicted to be HP (50.2%);
2. among all branches, actual HP (27%);
3. predicted LP while turn out to be HP (1.3%);
Performance
Analysis
3.1 Penalty Predictor
Average penalty of branches predicted LP: 121
HP: 212 cycles
%
covers 98.7% actual HP
Notes: This diagram is for penalty predictor. The X axis is for individual benchmarks and their average. The Y axis is percentage.
Let’s have a look at the average first. The height of the overall bar means the percentage of branches that predicted to be HP. The height of the lower gray bar means among all branches, the percentage that actually HP. The depth of black bar below X axis is the percentage that predicted LP while turn out to be HP.
If we regard the third number 1.3% as false negative, then the true positive will be 98.7% which also means our predicted HP branches have covered 98.7% actual HP branches.
In addition, the average penalty of predicted HP branches is almost double that of LP branches.

## Slide 9
Chart: 
| 8K | 16K | 32K | 64K | 128K | 256K
LTAGE | 0.038941 | 0.037009 | 0.035806 | 0.035077 | 0.03461 | 0.034353
PSLTAGE | 0.038895 | 0.036969 | 0.035769 | 0.035021 | 0.034539 | 0.03427
Chart: 
| 8K | 16K | 32K | 64K | 128K | 256K
LTAGE | 0.03647 | 0.034433 | 0.032942 | 0.032133 | 0.031505 | 0.030917
PSLTAGE | 0.036543 | 0.034346 | 0.032964 | 0.032161 | 0.031508 | 0.030961
3.2 Two-class TAGE predictor
MR
Performance
Analysis
1. MR of HP branches is about 10% higher;
All negative
2. Penalty-Sensitive (PS) method effectively favors HP branch;
3. 64KB: HP, -6E-5; LP, +3E-5.
Overall, it is beneficial.
Loop branches; branches with cache misses
Notes: This shows the MR of Two-class TAGE predictor. Since Two-class TAGE predictor can favor high-penalty branches, the MR of predicted both high-penalty and low-penalty branches is shown separately here.
The left diagram is for low-penalty branches. The right is for high-penalty branches.
The X axis shows TAGE predictor with different storage budget.
The yellow bar is for original LTAGE, while the red bar is for Penalty-Sensitive LTAGE.
From these two diagrams, we can observe three interesting points.
First, the MR of high-penalty branches is about 10% higher than that of low-penalty ones. There are two possible reasons. The first one is loop branches. Loop branches are usually low penalty. And their misprediction rate is very low. The second one is for branches with cache misses. Their penalty is very high, while there are usually hard to predict.
Second, all these numbers, which is the difference between the red bar and the yellow one, are negative. By the way, these number means the difference between the red bar and the yellow bar. This clearly tells us that the penalty-sensitive mechanism successfully favors HP branches, although the effect might be limited.
Third, take the configuration of 64KB for example. With our penalty sensitive mechanism, the MR of HP branches decrease, while that of LP branches increase. However, the difference of LP branches is only half that of HP ones. Furthermore, HP branches are more harmful. So, overall, our penalty sensitive mechanism is beneficial. It is the same for other configurations.

## Slide 10
4 Summary
Our penalty-sensitive branch predictor works
Penalty predictor: 50.2% predicted HP; covers 98.7% actual HP
Average penalty ( HP VS LP= 212: 121)
Two-class TAGE predictor: favor HP branches, globally beneficial, but limited
Limited favoring mechanism:
Double-entry allocation for HP branches to increase the chance that their new entries will survive longer time to establish usefulness.
Future: more helpful favoring mechanism needed
Conclusion:
2. Even if total MR doesn’t decrease, performance could still be improved by favoring HP branches;
1. Mispredicted HP branches are more harmful;
3. Can be applied to any predictors once we can find an effective favoring mechanism.
Notes: Finally, let me summarize this paper.
Our penalty-sensitive branch predictor works. For the penalty predictor, 50.2% branches are predicted as HP. It covers 98.7% actual HP branches. For the average penalty, HP branches is almost double that of LP ones.
The Two-class TAGE predictor favors HP branches obviously and globally beneficial. However, the performance improvement is limited. The reason is because of our limited favoring mechanism. Double-entry allocation for HP branches to increase the chance that their new entries will survive longer time to establish usefulness. This does not help much. In the future, more helpful favoring mechanism is needed.
In conclusion, our paper proposed an idea that mispredicted HP branches are more harmful, so even if the total MR doesn’t decrease, performance could still be improved by favoring HP branches. This idea can be applied to any predictors once we can find an effective favoring mechanism.

## Slide 11
Thanks!
Question & Answer
Notes: Thanks. Any question?

## Slide 12
Chart: 
| CL01 | CL02 | CL03 | CL04 | CL05 | CL06 | CL07 | CL08 | CL09 | CL10 | CL11 | CL12 | CL13 | CL14 | CL15 | CL16 | INT01 | INT02 | INT03 | INT04 | INT05 | INT06 | MM01 | MM02 | MM03 | MM04 | MM05 | MM06 | MM07 | SER01 | SER02 | SER03 | SER04 | SER05 | WS01 | WS02 | WS03 | WS04 | WS05 | WS06 | Average
Lo_AvgPen | 162.51 | 84.36 | 105.63 | 154.48 | 127.99 | 124.51 | 147.95 | 91.2 | 98.23 | 140.19 | 91 | 112.74 | 121.16 | 186.24 | 138.64 | 124.64 | 80.59 | 86.59 | 317.4 | 97.65 | 85.99 | 87.31 | 101.95 | 104.15 | 99.7 | 101.86 | 98.51 | 99.45 | 117.61 | 82.77 | 148.3 | 144.02 | 165.42 | 162.92 | 108.05 | 138.1 | 118.58 | 68.16 | 110.99 | 103.12 | 121.0165
Hi_AvgPen | 185.52 | 153.62 | 154.65 | 137.57 | 139.28 | 283.54 | 156.36 | 139.93 | 113.46 | 157.05 | 130.1 | 147.87 | 188.61 | 202.52 | 147.76 | 154.94 | 108.85 | 115.02 | 215.08 | 1830 | 123.66 | 121.93 | 199.4 | 191.28 | 146.16 | 170.22 | 123.86 | 119.55 | 266.92 | 157.87 | 181.11 | 174.49 | 244.96 | 271.03 | 149.7 | 280.71 | 192.95 | 156.04 | 187.33 | 224.85 | 213.6437
Penalty Predictor
Backup Slides
12

## Slide 13
Chart: 
| 8K | 16K | 32K | 64K | 128K | 256K
LTAGE | 0.038941 | 0.037009 | 0.035806 | 0.035077 | 0.03461 | 0.034353
PSLTAGE | 0.038895 | 0.036969 | 0.035769 | 0.035021 | 0.034539 | 0.03427
Chart: 
| 8K | 16K | 32K | 64K | 128K | 256K
LTAGE | 0.03647 | 0.034433 | 0.032942 | 0.032133 | 0.031505 | 0.030917
PSLTAGE | 0.036543 | 0.034346 | 0.032964 | 0.032161 | 0.031508 | 0.030961
Two-class TAGE predictor
MR
-6E-5
-4.7E-4
= 12.8%
-6E-5
-4.7E-4
Penalty-Sensitive achieved 12.8% improvement on MR of HP Branch that would be achieved by doubling storage budget.
Backup Slides
13

## Slide 14
Loop Predictor
Chart: 
| Client01 | Client02 | Client03 | Client04 | Client05 | Client06 | Client07 | Client08 | Client09 | Client10 | Client11 | Client12 | Client13 | Client14 | Client15 | Client16 | int01 | int02 | int03 | int04 | int05 | int06 | mm01 | mm02 | mm03 | mm04 | mm05 | mm06 | mm07 | server01 | server02 | server03 | server04 | server05 | ws01 | ws02 | ws03 | ws04 | ws05 | ws06 | Average
PSTAGE(without loop) | 188.401 | 3673.3317 | 132.8438 | 738.627 | 493.8692 | 99.6305 | 526.9068 | 175.5859 | 302.7089 | 310.6462 | 161.8361 | 489.4985 | 148.6496 | 278.3715 | 384.6467 | 245.0321 | 1642.7845 | 2208.1537 | 8.1515 | 24.5549 | 480.2687 | 483.4281 | 716.1345 | 695.8414 | 733.9024 | 651.1987 | 2839.4569 | 14.5433 | 8204.0034 | 660.0712 | 357.7047 | 308.6375 | 390.3974 | 402.0292 | 631.7523 | 682.2441 | 6624.2106 | 2592.1159 | 122.8704 | 174.9591 | 1000
PSLTAGE | 188.4369 | 3596.6291 | 132.8607 | 738.632 | 493.8692 | 99.6305 | 525.5694 | 175.6122 | 269.4566 | 310.6582 | 161.4421 | 489.4976 | 148.4949 | 273.9483 | 383.8666 | 244.9291 | 1642.8408 | 2207.9583 | 8.1515 | 23.8722 | 480.2755 | 483.4325 | 714.919 | 694.0545 | 733.6248 | 646.8488 | 2839.2359 | 14.3614 | 7919.7031 | 660.0738 | 357.3117 | 308.8476 | 390.4077 | 402.0383 | 631.1263 | 681.257 | 6630.2423 | 2515.7878 | 122.8761 | 174.9727 | 987.9438
1.3% Improvement with only 0.53KB
MPPKI
Average MPPKI normalized to 1000
Very
efficient
Backup Slides
14