## Slide 1: A 64 Kbytes ISL-TAGE predictor
André Seznec
INRIA/IRISA

## Slide 2: Build on L-TAGE
L-TAGE:
  TAGE + loop predictor
ISL-TAGE:
  TAGE + loop predictor
  + Statistical Corrector Predictor
  +Immediate Update Mimicker
  + tricks to try to win
500-800 MPPKI range

## Slide 3: TAGE: multiple tables, global history predictor
The set of history lengths forms a geometric series
What is important: L(i)-L(i-1) is drastically increasing
most of the storage
for short history !!
{0, 2, 4, 8, 16, 32, 64, 128}
Capture correlation
on very long histories

## Slide 4: TAGE Geometric history length + PPM-like + optimized update policy
pc
h[0:L1]
ctr
u
tag
hash
hash
=?
ctr
u
tag
hash
hash
=?
ctr
u
tag
hash
hash
=?
prediction
pc
pc
h[0:L2]
pc
h[0:L3]
1
1
1
1
1
1
1
1
1
Tagless base
predictor

## Slide 5
=?
=?
=?
1
1
1
1
1
1
1
1
1
Hit
Hit
Altpred
Pred
Miss

## Slide 6: Prediction computation
General case:
  Longest matching component provides the prediction
Special case:
  Many mispredictions on newly allocated entries: weak Ctr
  On many applications, Altpred more accurate than Pred
  Property dynamically monitored through a single 4-bit counter

## Slide 7: A tagged table entry
Ctr: 3-bit prediction counter
U: 1 useful bit
  Was the entry recently useful ?
Tag: partial tag
Tag
Ctr
U

## Slide 8: Allocate entries on mispredictions
Allocate entries in longer history length tables
  On tables with U unset
Set Ctr to Weak and U to 0
HUGE STORAGE BUDGET:
  Up to 4 entries allocated in different tables
    Fast warming

## Slide 9: Managing the (U)seful bit
Setting when avoids a misprediction
    (Pred = taken) & (Alt ≠ taken)
Global reset when « difficulties » to allocate
  Dynamically monitor if more failures than successes on allocations
7 MPPKI +
29 Kbits

## Slide 10: The loop predictor
Predict loop with constant number of iterations:
  64 entries
  less than 6 bytes per entry
  Capture some behavior that TAGE is not able
12 MPPKI

## Slide 11: The Immediate Update Mimicker
Issue:
  Some mispredictions due to late updates at retirement
Immediate Update Mimicker:
  Try to catch these cases

## Slide 12: The Immediate Update Mimicker
P
T
A
Same table, same entry
E
T
A
E
T
A
E
T
A
P
T
A
P
T
A
E
T
A
P
T
A
E
T
A
P
T
A
P
T
A
P
T
A
P
T
A
P
T
A
Misprediction
P(rediction) or (E)xecuted
T(able)
A(ddress in the table)
P
T
A
P
T
A
P
T
A
P
T
A
P
T
A
P
T
A
P
T
A
P
T
A
P
T
A
P
T
A
P
T
A
P
T
A
Fetch
7 MPPKI

## Slide 13: The Statistical Corrector predictor
Branches with poor correlation with history:
  Sometimes better predicted by a single wide PC indexed counter than by TAGE
More generally, track cases such that:
  « In this case (PC, history, prediction),
  TAGE is likely (>50 %) to mispredict »

## Slide 14: The Statistical Corrector Predictor
Main
(TAGE +IUM)
Predictor
H
A
Stat.
Corr.
Prediction + counter value
Loop Predictor

## Slide 15
Main
(TAGE +IUM)
Predictor
H
A
Stat
Cor.
Loop
+
H
A
Pred
counter value

## Slide 16: The Statistical Corrector Predictor for the contest
Derived from the GEHL predictor:
  5 (logic) tables sharing 4K 6-bit entries
  + use TAGE prediction in the index
  + values of the provider counter
Use prediction when
    |sum| > dynamic threshold
15 MPPKI

## Slide 17: Dimensioning TAGE
Huge storage budget:
  15 tagged tables + the bimodal
  Different tag width
  All branches + path
  (6,2000) history
  + extra bits for indirect and calls
5 MPPKI

## Slide 18: For the competition: interleaving
=?
=?
=?
prediction
Xbar
Xbar
h[0,L1]
h[0,L1]
6 MPPKI

## Slide 19: For the competition
Guided selection of the best set of history lengths:
  0, 3, 8, 12, 17, 33, 35, 67, 97, 138, 195, 330, 517, 1193, 1741, 1930
3 MPPKI

## Slide 20: All these efforts for 43 MPPKI
+10
16KB ISL-TAGE
64KB CBP2 L-TAGE
Ref
32KB ISL-TAGE
-24
64KB ISL-TAGE
-43
-113
LIMIT ISL-TAGE
-49
LIMIT CBP2 L-TAGE
MPPKI

## Slide 21: Missed opportunity (in the submitted predictor)
Statistical Predictor
  Could accomodate local history
16 MPPKI
And loop predictor becomes (almost) useless

## Slide 22: Summary
ISL-TAGE built on top of TAGE:
  Loop predictor
  Immediate Update Mimicker
    Uses information that must be propagated
  Statistical Corrector Predictor
    Opens opportunity to uses local history
  + unrealistic interleaving